University of Massachusetts Lowell

600 Suffolk St

Lowell, Massachusetts 01854

Phone 978-934-4900

Fax 978-459-7915

UMLCAR

RPI Commands

A description of the flight/development commands used in communications between ASIST and RPI.

Version 1.1

# Table of Contents

Table of Contents	2

Table of Acronyms	3

RPI Mnemonic Label Naming Conventions	4

1.	Data Block Uploads	5

1.1.	Control of RPI automated operation	5

1.2.	RPI software upgrades	6

2.	Pass-Through Command Messages	6

2.1.	RPI Status Commands	7

2.2.	Saving contents of RPI SRAM in RPI EEPROM	7

2.3.	RPI Operational Commands	7

2.4.	Initiation of requests to CIDP	8

3.	Standard CIDP Command Messages	9

4.	RPI Development commands	10

4.1.	Mnemonics for Development Commands	10

4.2.	Development Package Formats	12

4.2.1.	ApID=0x90 Frequency Set Response Package	12

4.2.2.	ApID=0x91 Memory Read/Write Response Package	13

4.2.3.	ApID=0x92 VME Read/Write Response Package	14

4.2.4.	ApID=0x93 Digitizer Samples Package	14

# Table of Acronyms

ApID	Application ID (identifier added to data packets)

ASIST	The Advanced System for Integration and Spacecraft Test

BIT	Built In Test

CIDP	Central Instrument Data Processor

EEPROM	Electrically Erasable Programmable Read-Only Memory

GSEOS	Ground Support Equipment Operating System

HK		House Keeping

IMAGE	Imager for Magnetopause-to-Aurora Global Exploration

LTD		Linear Time Domain

RPI		Radio Plasma Imager

SCU	Spacecraft Computer (the computer which controls S/C flight functions)

SI	Science Instrument

SRAM	Static Random Access Memory

UML	University of Massachusetts Lowell

UMLCAR	University of Massachusetts Lowell Center for Atmospheric Research

UTC	coordinated universal time

UUT	unit under test

VME	Virtual Memory Environment – “Eurobus” standard interface for computer boards

.

# RPI Mnemonic Label Naming Conventions

| Mnemonic Name | Label | Description |
| --- | --- | --- |
| Field 1 |  |  |
| Instrument Identifier | R_ | Assigned to RPI Commands |
| Field 2 |  |  |
| Affected component | MEM_ | Affects SRAM or EEPROM memory contents |
| or mode | STA_ | System Status Information |
|  | SYS_ | System (general on-orbit commands) |
|  | REQ_ | Request to CIDP |
|  | DEB_ | Debugging/Testing Commands for Engineering Development |
| Field 3 |  |  |
| Affected Subcomponent | HK | Built in self-test sensors, or preprogrammed test routines |
|  | SEG | A segment of memory, designated by a numeral |
|  | PROG | Program |
|  | SCHD | Schedule |
|  | SST | Schedule Start Time |
|  | TIME | Mission Elapsed Time (4 byte integer, in 0.1 sec units) |
|  | PORT | Any RPI Latch located at given VME port number |
|  | FREQ | Synthesizer & Preselector control bytes (operating freq) |
|  | PLIM | System power consumption limit |
|  | DATA | Data |
|  | DGTZ | Digitizer |
|  | CPLR | Antenna coupler |
| Field 4 |  |  |
| Action | SET_ | Write only the designated bits in an RPI hardware latch(es) |
|  | WRIT_ | Write given byte into RPI hardware latch(es) |
|  | CLR_ | Clear only the designated bits in an RPI hardware latch(es) |
|  | LOAD_ | Copy message contents into RPI RAM |
|  | SEND_ | Causes RPI to send information which ALREADY EXISTS |
|  | GET_ | Causes RPI to take some action THEN send information |
|  | RUN_ | Executes a pre-programmed function |
|  | SAVE_ | Move contents of RAM to EEPROM for permanent storage |

RPI Flight Commands

The following sections introduce and describe the commands designed to control the RPI instrument during the mission time. These formats are intended for external use and distribution for general control of the RPI instrument on flight.

# Data Block Uploads

The standard Data Block Upload mechanism (see CIDP to SI Interface Control Document, section 4.1.3.2.2.6) is used to perform most of the RPI flight commanding. The SRAM of RPI is divided into enumerated segments of variable size. One SRAM segment is the smallest unit that can be uploaded during on-orbit operation.

A single Data Block Upload command may contain contents of more than one segment. To accommodate this feature, segment addresses and lengths are included in the body of the command (i.e., the data block). Thus, the addressing parameters in the first packet of the standard Data Block Upload command sequence are not used by RPI.

## Control of RPI automated operation

Some “pass-through” control commands are provided (see Section 2) for immediate RPI action, but most of the operation of the RPI instrument is scheduled and controlled by uploading the contents of three control data structures:

- 64 Programs [3264 bytes],

- 32 Schedules [3872 bytes],

- 256 Schedule Start Times (SST) [1280 bytes],

and one system configuration structure:

- ARMENU [TBD bytes],

using the standard Data Block Upload mechanism.

At any time, RPI will function automatically, according to the currently active schedule. Each schedule specifies a sequence of measurement programs which is repeated by RPI. The schedule remains active until a valid schedule start time (SST) activates another schedule, or an SST table expiration time starts one of the default schedules. Schedule 0 is always empty so it puts RPI in an idle state.

System configuration structure contains a set of Red Limit checking specifications, data content selection for the real-time NOAA telemetry channel, and a table of restricted frequencies.

Each control data structure takes a single SRAM segment. No provision is made for changes to the individual parts of the three control data structures and the system configuration, with the exception of adding a single entry to the SST table via R_OPR_SET_SST command.

## RPI software upgrades

Upgrades to the RPI software are done by replacing contents of SRAM segments. Each software segment starts with a set of pointers to the public procedures in the segment. The rest of RPI software routines call the public procedures via these pointers. This mechanism allows updating of the contents of individual segments without changing any of the other software segments. Once the upgraded software has been evaluated to run successfully it will be copied over, upon receipt of a R_MEM_SEG_SAVE command from the ground, into the two independent banks of EEPROM, thereby becoming the operating software which will be loaded at next power-on.

If a change is made to the starting address of a segment in SRAM or the number of public procedures available in a segment, all software segments that access the public procedures in the changed segment would have to be updated as well.

# Pass-Through Command Messages

RPI Pass-Through command messages are received by the CIDP from the SCU and forwarded to RPI as 64-byte Ground Commands of the format shown in Table 2-1.

Table 2-1  Pass-Through Command Messages

| Byte # | Description | Hex value | Comments |
| --- | --- | --- | --- |
| 0..2 | Sync Pattern | FEFA30 |  |
| 3 | Header | CC |  |
| 4 | Checksum |  | bytes 5..61 |
| 5 | Byte count |  | starting at byte 6 |
| 6 | Command Stem |  |  |
| 7..63 | Command Parameters |  |  |

There are four categories of RPI Pass-Through commands described in the section 2.1-2.4:

- Status commands

- EEPROM save command

- Operational commands

- CIDP command requests

## RPI Status Commands

RPI status commands include collection of housekeeping information in ApID=0x02 packages and reports of SRAM and EEPROM segment contents in ApID=0x04 packages. Table 2-2 shows a description of the status commands.

Table 2-2  RPI Status Commands

| Mnemonic | Command stem and arguments | Description |
| --- | --- | --- |
| R_HK_BIT_RUN | 0x45 | RPI will execute a Built-In Test routine, then report the results in ApID=0x02 housekeeping package |
| R_HK_BIT_SEND | 0x46 | RPI will report the latest available Built-In Test parameters in ApID=0x02 housekeeping package |
| R_BIT_SEG_SEND | 0x49 | RPI will send the memory dump of the specified segment in ApID=0x04 housekeeping packages. |
| ARG1 | SEG= [unsigned char] | Segment number |

## Saving contents of RPI SRAM in RPI EEPROM

The remote update of software and control data structures is done to RPI SRAM. Once the changes are proved to operate correctly, the contents of RPI RAM segments can be stored permanently in RPI EEPROM (and therefore the changes are not lost if RPI is rebooted).

The memory segments can be saved to EEPROM individually or in groups (all software, all control data structures) as described in Table 2.3.

Table 2-3  Saving SRAM to EEPROM Command

| Mnemonic | Command stem and arguments | Description |
| --- | --- | --- |
| R_MEM_SEG_SAVE | 0x4A | Contents of the specified SRAM segment(s) are copied to RPI EEPROM. |
| ARG1 | SEG= [signed char] | -1 save all SRAM software -2 save all control data structures (0 save the specified segment |

## RPI Operational Commands

RPI implements a set of commands used for on-orbit operation as described in the Table 2-4.

Table 2-4  RPI Operational Commands

| Mnemonic | Command stem and arguments | Command Description |
| --- | --- | --- |
| R_SYS_CPLR_RUN | 0x31 | Perform antenna coupler rattle |
| R_SYS_SST_SET | 0x32 | Add SST to the RPI SST queue. NOTE: The RPI software will locate the SST in a time ordered stack, so there is no “SST request number” |
| ARG1 | MET= [4 bytes] | MET at which to switch schedule (4-bytes) |
| ARG2 | SCHD= [unsigned byte] | Schedule # to take effect at the given MET |
| R_SYS_PLIM_SET | 0x38 | Set operational power limits (and override the limits specified in RPI program) |
| ARG1 | PEAK= [unsigned byte] | Peak power during transmission, in Watts (1-byte) |
| ARG2 | AVG= [unsigned byte] | Energy over 1-hour/3600sec, i.e. Watts (1-byte) |
| R_SYS_PWR_LOW | 0x81 | Power Low message, duplicate to the standard CIDP command 0xD1. The CIDP command is available only as a broadcast to all instruments. |
| R_SYS_PWR_NOM | 0x82 | Nominal Power message, duplicate to the standard CIDP command 0x1D. The CIDP command is available only as a broadcast to all instruments. |
| R_SYS_PWR_OFF | 0x84 | Power Off |

## Initiation of requests to CIDP

Table 2-5   Requests to CIDP

| Mnemonic | Command stem and arguments | Description |
| --- | --- | --- |
| R_REQ_DATA_LOAD | 0x50 | Request upload of a CIDP EEPROM block contents to RPI (standard SI-to-CIDP requests 0x05, 0x15, 0x25 and 0x35) |
| ARG1 | BLK= [unsigned byte] | CIDP EEPROM block number |
| R_REQ_PWR_OFF | 0x57 | Send Power Off request 0x11 to CIDP |
| R_REQ_PWR_CYCL | 0x59 | Send Power Cycle request 0x12 to CIDP |

# Standard CIDP Command Messages

RPI operations rely on availability of the standard CIDP command messages listed in the Table 3-1.

Table 3-1  Standard CIDP commands essential to RPI Operations

| Message Name | Header | Relevant CIDP Mnemonics |
| --- | --- | --- |
| SAFE | 0xDD | C_SIRPI_PWR_SAFE C_SIALL_PWR_SAFE |
| LOW POWER | 0xD1 | C_SI_BCST_LOP |
| NOMINAL POWER | 0x1D | C_SI_BCST_HIP |

RPI Development Commands

The following sections introduce and describe the commands for controlling and testing of the RPI instrument. These formats are intended for debugging, fault detection, analysis, and hence are implemented for exclusive use of the RPI engineering team. These commands are not intended for general control of RPI on flight.

# RPI Development commands

The development commands are stored in the ASIST database and are used during Payload and Observatory testing phase. Some of development commands result in output of development data packages (ApID=0x90, 0x91, and 0x92) to telemetry stream. The development commands will not be needed on orbit, but the RPI Flight software will continue to recognize them in order to maintain software configuration, and to provide options for on-orbit troubleshooting.  The ability to indiscriminately use the development  commands for on-orbit operations should however, be blocked in the ASIST software (e.g. by recognizing the “DEB_” in the Mnemonic name).

## Mnemonics for Development Commands

Table 4-1   Mnemonics for Development (DEBUG) Commands

| Mnemonic | Command stem and arguments | Description |
| --- | --- | --- |
| R_DEB_FREQ_SET | 0x70 | Sets freq synthesizer, receiver preselectors and antenna coupler. Send new settings in ApID=0x90 development package. |
| ARG1 | FREQ= [32 bit] | Frequency in Hz |
| ARG2 | MODE= [unsigned byte] | Coupler mode: 0 or ‘N’ Normal (i.e. Tuned) setting of the Antenna Coupler 1 or ‘D’ Direct (i.e. not-Tuned), selects Bypass setting in antenna coupler 2 or ‘C’ Calibrate, selects calibration signal path in antenna coupler 3 or ‘S’ Same as 2, does not command antenna coupler |
| R_DEB_MEM_SEND | 0x71 | Perform generic read/write operation with a block of RPI memory. RPI will send an ApID=0x91 development package in response to the command. |
| ARG1 | MODE= [8 bit] | ‘W’ Write ‘R’ Read |
| ARG2 | ADDR1= [32 bit] | Starting address |
| ARG3 | ADDR2= [32 bit] | Ending address |
| ARG4 | VALUE= [32 bit] | the value to write (for write commands only) |
| R_DEB_PORT_SEND | 0x72 | Sends ARG3 value (byte) to VME port address ARG2 in mode ARG1. The command results in output of development package ApID=0x92 with port status information. |
| ARG1 | MODE= [8 bit] | ‘R’ Read from ARG2 ‘W’ Write ARG3 to ARG2 ‘S’ Set bits indicated by 1’s in ARG3 mask at location ARG2 ‘C’ Clear bits indicated by 1’s in ARG3 mask at location ARG2 ‘I’ Invert (complement) bits indicated by 1’s in ARG3 mask at location ARG2 ‘T’ Toggle (invert twice) bits indicated by 1’s in ARG3 mask at location ARG2 |
| ARG2 | ADDR= [32 bit] | VME address, 32-bit hexidecimal |
| ARG3 | VALUE= [8 bit] | 8-bit “port specific” latch contents |
| R_DEB_DGTZ_GET | 0x73 | Starts acquisition of digitizer samples and continues until new commands arrives to interrupt it. (Data is returned in special “developmental” format packages (see ApID 0x93 below). |
| ARG1 | BFR= [8 bit] | Buffer number, see Table 4-2 |
| ARG2 | BITS= [32 bit] | Bit Bits, see Table 4-2 |
| R_DEB_SCHD_SET | 0x74 | Activates the specified schedule. Currently active program is interrupted and a new program starts as specified by the new schedule |
| ARG1 | SCHD= [unsigned byte] | # Schedule number (0-31) |
| R_DEB_CAL_OFF | 0x75 | Calibration OFF. Next program will be executed with no correction of receiver gain or phase. The program after that will return to the automatic calibration. |
| R_DEB_TIME_SET | 0x76 | Changes system time to the given MET (4-bytes) |
| ARG1 | MET= [32 bit] |  |
| R_DEB_LTD_RUN | 0x77 | Sets up a pre-determined loopback calibration program, acquires data and outputs in ApID=0x30 (LTD) packages |
| ARG1 | PROG= [unsigned byte] | Program number (0-63) |

Table 4-2   Buffer Number and Bit Bits combinations for R_DEB_DGTZ_GET command

| Buffer No. | 0 | 1 | 2 | 3 |
| --- | --- | --- | --- | --- |
| Bit Bits |  |  |  |  |
| 0 | X Ant. Samples | Y Ant. Samples | Z Ant. Samples | IFSmp & RFSmp |
| 2 | IFSMPZ + 400KB | IFSMPY + XVARI | 2500B + YVARI | GND + MUX1 |
| 3 | XMTR2B + C140KB | LOB + 10.56B | SYSTEMP + 95KB | X+TMP + XMTR1B |
| 7 | Y+TMP + RFX+ | Y-TMP + RFX- | ZTEMP + RFY+ | RFY- + Y+TMP |

## Development Package Formats

RPI responds to certain development commands by outputting Development Package(s) to the RS-422 port (to be received by CIDP, GSEOS, ASIST, etc.). All development packages are formatted as standard Science Data Packages, however, they are unlikely to be used during the mission time.

### ApID=0x90 Frequency Set Response Package

The frequency set command R_DEB_FREQ_SET is acknowledged by a message giving the programmed frequency, the coupler mode character, the relay settings for all four couplers, the synthesizer control byte settings, and the preselector control byte setting (see Table 4-3).

Table 4-3   Frequency Set Response package, ApID=0x90

| Byte No. | Name | Value | Comments |
| --- | --- | --- | --- |
| 0..2 | Sync pattern | FEFA30h |  |
| 3 | Header | 0xDC | Data package |
| 4 | ApID | 0x90 |  |
| 5..6 | Byte Count | 21 | (constant) |
| 7-10 | Frequency | f<31:24> |  |
|  |  | f<23:16> | Sounding frequency in Hz. |
|  |  | f<15:8> |  |
|  |  | f<7:0> |  |
| 11 | Coupler mode | ‘N’ - normal ‘D’ - direct ‘C’ - calibrate ‘S’ - calibrate-direct | This character indicates whether a special coupler mode has been selected. |
| 12..13 | Xplus relays | <15:8> <7:0> | This 16-bit value indicates the states of the 16 relays in this antenna coupler. Bit zero equals 1 if relay K1 is on; bit 1 is 1 for relay K2, etc. |
| 14..15 | Xminus relays | <15:8> <7:0> | This 16-bit value indicates the states of the 16 relays in this antenna coupler. Bit zero equals 1 if relay K1 is on; bit 1 is 1 for relay K2, etc. |
| 16..17 | Yplus relays | <15:8> <7:0> | This 16-bit value indicates the states of the 16 relays in this antenna coupler. Bit zero equals 1 if relay K1 is on; bit 1 is 1 for relay K2, etc. |
| 18..19 | Yminus relays | <15:8> <7:0> | This 16-bit value indicates the states of the 16 relays in this antenna coupler. Bit zero equals 1 if relay K1 is on; bit 1 is 1 for relay K2, etc. |
| 20 | Reg5 |  |  | LO freq = Reg5*125 kHz |
| 21 | Reg4 |  | Synth. | + Reg4*125 khz / 28 |
| 22 | Reg3 |  | Control | + Reg3*125 kHz / 216 |
| 23 | Reg2 |  | Registers | + Reg2*125 kHz / 224 |
| 24 | Reg1 |  |  | + Reg1*125 kHz / 232 |
| 25 | Reg0 |  |  | + Reg0*125 kHz / 240 |
| 26 | Data Byte “n” | pfrq | Preselector control byte |
| 27 | Checksum |  | xor sum bytes 7-26 |

### ApID=0x91 Memory Read/Write Response Package

The memory read/write command reply gives the starting and ending addresses of the memory block followed by the contents of the block. The format for the memory read/write command reply message is given in Table 4-4.

Table 4-4   Memory Read/Write Response package, ApID=0x91

| Byte No. | Name | Byte Value | Comments |
| --- | --- | --- | --- |
| 0..2 | Sync pattern | FEFA30h |  |
| 3 | Header | 0xDC | Data package |
| 4 | ApID | 0x91 |  |
| 5..6 | Byte Count |  | Byte Cnt = 10 + 4*(Addr2-Addr1+1) |
| 7 | Data Byte 0 | ‘R’ or ‘W’ | ‘R’ = memory block read, ‘W’ = memory block write |
| 8..11 | Starting Address | <31:24> <23:16> <15:8> <7:0> | Starting address of memory block to be read/written |
| 12..15 | Ending Address | <31:24> <23:16> <15:8> <7:0> | Ending address of memory block to be read/written |
| 16..19 | Data 1 | <31:24> <23:16> <15:8> <7:0> | 32 bit word |
| … | … | … | … |
| 15+4*n |  | Checksum | xor sum bytes 7-19 |

### ApID=0x92 VME Read/Write Response Package

The VME Read/Write response package returns the VME address and contents for the affected VME port.  The format for the VME read/write command reply message is given in Table 4-5.

Table 4-5   VME Read/Write Response package, ApID=0x92

| Byte No. | Name | Byte Value | Comments |
| --- | --- | --- | --- |
| 0..2 | Sync pattern | FEFA30h |  |
| 3 | Header | 0xDC | Data package |
| 4 | ApID | 0x92 |  |
| 5..6 | Byte Count | 6 |  |
| 7..10 | Address | <31:24> <23:16> <15:8> <7:0> | VME Address of affected VME port.. |
| 11 | Value |  | Contents of affected VME port after VME Port command is executed. |
| 12 | Checksum |  | xor sum bytes 7-11 |

### ApID=0x93 Digitizer Samples Package

The acquire command R_DEB_DGTZ_GET continuously takes digitizer samples, sending back digitizer sample blocks as indicated below. Packets are transmitted continuously until RPI receives a new command.  The format for the Digitizer Samples package is shown in Table 4-6.

Table 4-6   Digitizer Sample package, ApID=0x93

| Byte No. | Name | Byte Value | Comments |
| --- | --- | --- | --- |
| 0..2 | Sync pattern | FEFA30h |  |
| 3 | Header | 0xDC | Data package |
| 4 | ApID | 0x93 |  |
| 5..6 | Byte Count | 4N+1 | N = number of complex samples |
| 7..8 | Real 1 | <15:8> <7:0> | First real sample |
| 9..10 | Imaginary 1 | <15:8> <7:0> | First imaginary sample |
| 11..12 | Real 2 | <15:8> <7:0> | Second real sample |
| 13..14 | Imaginary 2 | <15:8> <7:0> | Second imaginary sample |
| … | … | … | … |
|  | Real N | <15:8> <7:0> | Nth real sample |
|  | Imaginary N | <15:8> <7:0> | Nth imaginary sample |
| 4N+6 | Checksum |  | xor sum |

# Text boxes

November 6, 1998